PANASONIC WV-X86531-Z2 MULTI PTZ DOME NETWORK CAMERA

TECHNICAL SPECIFICATIONS

DIVISION 28 – ELECTRONIC SAFETY AND SECURITY

28 20 00 ELECTRONIC SURVEILLANCE

28 23 00 VIDEO SURVEILLANCE

28 23 29 VIDEO SURVEILLANCE REMOTE DEVICES AND SENSORS

This specification is intended for use by the design/construction professional and any user of Panasonic Security products to assist in developing project specifications for security and video surveillance systems.

Specifier Notes:  This guide specification incorporates CSI MasterFormatTM 2014 Edition Numbers and Titles.

Notes in Italics, such as this one, are explanatory and intended to guide the design professional/specifier and user in the proper selection and use of materials. This specification should be modified where necessary to accommodate individual project conditions.

PART 1 GENERAL

  - SUMMARY

  - WARRANTY

- Provide manufacturer's standard warranty.

# PART 2 PRODUCTS

- MANUFACTURERS

  - Panasonic i-PRO Sensing Solutions Co., Ltd

  - Provide Video Surveillance Camera from single source manufacturer

- PANASONIC WV-X86351-Z2 MULTI PTZ DOME NETWORK CAMERA

  - GENERAL CHARACTERISTICS

    - The multi-sensor/PTZ combination camera will be a single factory assembled unit consisting of a pan/tilt/zoom camera element and a 4 lens multi-sensor camera element.

    - The multi-sensor/PTZ camera will use a single RJ-45 Ethernet LAN.

    - FIPS 140-2 level 3 certified*Built-in EdgeLock® SE050F (NXP®Semiconductors) connection to access both camera elements.

    - The multi-sensor element with be factory calibrated with the PTZ camera and not require field calibration between the multi-sensor and PTZ elements for point and click positioning.

    - It will be possible to access, control and configure the multi-sensor and PTZ elements separately using standard web browsers.

    - The multi-sensor/PTZ combo camera will be NDAA complaint.

    - The multi-sensor/PTZ camera will be FIPS 140-2 level 3 certified with built-in EdgeLock® SE050F (NXP®Semiconductors).

    - The multi-sensor/PTZ combo will be OnVIF Profiles S, T, G and M complaint.

- CAMERA

| Image Sensor | <Multi Part> 4x 1/2.7 type CMOS image sensor <PTZ Part> 1/2.8 type CMOS image sensor |  |
| --- | --- | --- |
| Minimum Illumination | <Multi Part> Color : 0.12 lx (30IRE,F2.0, 1/30 s) Color : 0.17 lx (50IRE,F2.0, 1/30 s) BW : 0.10 lx (50IRE,F2.0, 1/30 s) <PTZ Part> Color : 0.011 lx (30IRE,F1.6, 1/30 s) Color : 0.015 lx (50IRE,F1.6, 1/30 s) BW : 0.006 lx (50IRE,F1.6, 1/30 s) |  |
| White Balance | ATW1/ ATW2/ AWC |  |
| Shutter Speed | <Multi Part> 15 fps mode: Max.1/10000s to Max.16/30s <PTZ Part> 60 fps mode: Max.1/4000s to Max.16/30s 30 fps mode: Max.1/4000s to Max.16/30s 15 fps mode: Max.1/4000s to Max.16/30s |  |
| Intelligent Auto | On / Off |  |
| Super Dynamic | <Multi Part> On / Off, The level can be set in the range of 0 to 31. <PTZ Part> On / Off, The level can be set in the range of 0 to 31. *1 |  |
| Dynamic Range | <Multi Part> 108 dB max. (Super Dynamic: On, Level: 31) <PTZ Part> 144 dB max. (Super Dynamic: On, Level: 31) |  |
| Adaptive Black Stretch | The level can be set in the range of 0 to 255. |  |
| Back light compensation / High light compensation | BLC (Back light compensation) / HLC (High light compensation) / Off (only when Super dynamic / Intelligent Auto: Off) |  |
| Fog compensation | On / Off (only when Intelligent auto / auto contrast adjust: Off) |  |
| Maximum gain (AGC) | The level can be set in the range of 0 to 11. |  |
| Color/BW (ICR) | Off/On/Auto1(Normal)/Auto2(IR Light)/Auto3(SCC) |  |
| Digital Noise Reduction | The level can be set in the range of 0 to 255. |  |
| Video Motion Detection (VMD) | On / Off, 4 areas available |  |
| Scene Change Detection (SCD) | On / Off, 1 area available |  |
| Audio Detection | On / Off |  |
| AI Sound Classification | Selectable from Gunshot, Yell, Vehicle horn, Glass break |  |
| AI Analytics | AI Video Motion Detection, AI Privacy Guard, AI Face Detection, AI People Detection, AI Vehicle Detection, AI Non mask Detection, AI Occupancy Detection For details https://i-pro.com/global/en/surveillance/products/i-pro-ai-application 3rd party applications are also available. https://i-pro.com/global/en/surveillance/i-pro-application-platform/application-list |  |
| Privacy Zone | <Multi Part> On / Off, Up to 8 zones available <PTZ Part> On / Off, Up to 32 zones available |  |
| VIQS | <Multi Part> On / Off, Up to 8 zones available <PTZ Part> On / Off, Up to 8 zones available |  |
| Image Rotation | Upside-down: On / Off |  |
| Camera Title (OSD) | On/ Off, Up to 40 characters, Up to 2 Lines (alphanumeric characters, marks) |  |
| Focus Adjustment | <Multi Part> - <PTZ Part> Auto focus |  |
| LENS Optical zoom | <Multi Part> 1x <PTZ Part> 21x (Motorized zoom / Motorized focus) |  |
| Extra zoom | <Multi Part> max 4.0x (when resolution is 640x360) <PTZ Part> max 31x(when resolution is 1280x720) |  |
| Focal Length | <Multi Part> 3.2mm <PTZ Part> 4.0mm - 84.6mm｛5/32inches - 3-11/32 inches｝ |  |
| Angular Field of View | <Multi Part> Horizontal: 97 deg. Vertical: 71 deg. <PTZ Part> Horizontal: 3.7 ° to 77 ° Vertical: 2.2 ° to 44° |  |
| Maximum Aperture Ratio | <Multi Part> 2 <PTZ Part> 1：1.6（WIDE） to 1：4.5（TELE） |  |
| Focus Range | <Multi Part> 1 m {3.28 ft} to ∞ <PTZ Part> 1.5 m {59-1/16 inches} to ∞ |  |
| DORI Detect (25ppm / 8ppf) | <Multi Part> 45.3 m / 148.6 ft <PTZ Part> Wide: 48.3 m / 158.4 ft, Tele: 1188.9 m / 3900.5 ft |  |
| Observe (62.5ppm / 19ppf) | <Multi Part> 18.1 m / 59.4 ft <PTZ Part> Wide: 19.3 m / 63.4 ft, Tele:475.5 m / 1560.2 ft |  |
| Recognize (125ppm / 38ppf) | <Multi Part> 9.1 m / 29.7 ft <PTZ Part> Wide: 9.7 m / 31.7 ft, Tele: 237.8 m / 780.1 ft |  |
| Identify (250ppm / 76ppf) SYSTEM ON CHIP (SoC) System on Chip (SoC) | <Multi Part> 4.5 m / 14.9 ft <PTZ Part> Wide: 4.8 m / 15.8 ft, Tele: 118.9 m / 390.0 ft <Multi Part> Ambarella CV2 <PTZ Part> Ambarella CV25m |  |
| ADJUSTING ANGLE Adjusting Angle | <Multi Part> Camera 1, 2, 3, 4: Vertical: 40 ±7° (Adjust by vertical (TILT) angle) <PTZ Part> Horizontal: 360° Endless Panning / Vertical: -15 to +195°/ Yaw : 0° |  |
| PAN/TILT Panning Range | 360° Endless Panning |  |
| Panning Speed Tilting Range Tilting Speed Preset Positions Auto Mode Self-Return | Manual ： 0.065 °/s – 150°/s Preset ： Up to 500 °/s Operational -15 – +195° Manual ： 0.065 °/s – 150°/s Preset ： Up to 500 °/s 256 positions Auto Track / Auto pan / Preset sequence / Patrol 10 s/ 20 s/ 30 s/ 1 min/ 2 min/ 3 min/ 5 min/ 10 min/ 20 min/ 30 min/ 60 min |  |
| BROWSER GUI Camera Control | Brightness, AUX On / Off |  |
| Audio | Mic (Line) Input: On / Off Volume adjustment : Low / Middle / High Audio Output : On / Off Volume adjustment : Low / Middle / High |  |
| GUI/ Setup Menu Language Browser | English, Italian, French, German, Spanish, Portuguese, Russian, Chinese, Japanese Microsoft Edge, Firefox, Google Chrome |  |
| NETWORK |  |  |
| Network IF | 10 BASE-T/100 BASE-T/1000 BASE-T, RJ45 connector |  |
| Resolution H.265/ H.264 JPEG (MJPEG) | <Multi Part> [4:3] (15fps mode)/[4:3] (12.5fps mode) 3072 x 2304*2, 2560x1920, 1280 x 960, VGA, QVGA [4:3] (15fps Quad mode)/[4:3] (12.5fps Quad mode) 3072 x 2304*2, 2560x1920, 1280 x 960, VGA [16:9] (15fps mode) / [16:9] (12.5fps mode) 3072 x 1728*2, 2560x1440, 1920 x 1080, 1280 x 720, 640×360, 320×180 [16:9] (15fps Quad mode)/[16:9] (12.5fps Quad mode) 3072 x 1728*2, 2560x1440, 1920 x 1080, 1280 x 720, 640×360 <PTZ Part> ［16:9 mode (60 fps mode) ］［16:9 mode (30 fps mode) ］［16:9 mode (50 fps mode) ］［16:9 mode (25 fps mode) ］ 1920x1080,1280x720,640x360,320x180 ［4:3 mode (30 fps mode) ］［4:3 mode (25 fps mode) ］ 1280x960,VGA,QVGA ［4:3 mode (15 fps mode) ］［4:3 mode (12.5 fps mode) ］ 2048x1536*2,1280x960,VGA,QVGA |  |
| H.265/H.264 | [Transmission Mode] Constant bit rate / VBR / Frame rate / Best effort [Transmission Type] Unicast port (AUTO) / Unicast port (MANUAL) / Multicast |  |
| JPEG | [Image Quality] 10 steps |  |
| Smart Coding | GOP (Group of pictures) control: On (Frame rate control)* / On (Advanced)* / On (Mid) / On (Low) / Off *On (Frame rate control) and On (Advanced) are only available with H.265. Smart VIQS: On(High)/On(Low)/Off, Smart P-picture control: On/Off |  |
| Audio Compression | G.726（ADPCM）32 kbps/16 kbps, G.711 64 kbps, AAC-LC 64kbps/96kbps/128kbps *3 |  |
| Audio Transmission Mode | Off / Mic (Line) input / Audio output / Interactive (Half duplex) / Interactive (Full duplex) |  |
| Supported Protocol | IPv6： TCP/IP, UDP/IP, HTTP, HTTPS, SSL/TLS, SMTP, DNS, NTP, SNMPv1/v2/v3, DHCPv6, RTP, MLD, ICMP, ARP, IEEE 802.1X <Control No.: C0141> *4, DiffServ, LLDP, MQTT |  |
| No. of Simultaneous Users | <Multi Part> 24 (Number of sessions that can connect to cameras at the same time)* Depends on network conditions <PTZ Part> 14 (Number of sessions that can connect to cameras at the same time)* Depends on network conditions |  |
| Secure | FIPS 140-2 level 3 (NXP® EdgeLock® SE050F), Device Certificate GlobalSign® pre-installed, User authentication, Host authentication, HTTPS, 802.1X Support <Control No.: C0141> *4 |  |
| SDXC/SDHC/SD Memory Card | microSDXC memory card：64 GB, 128 GB, 256 GB, 512 GB microSDHC memory card：4 GB, 8 GB, 16 GB, 32 GB microSD memory card ：2 GB |  |
| Mobile Terminal Compatibility | iPad, iPhone (iOS 8.0 or later), Android™ terminals |  |
| ONVIF® Profile ALARM | G / M / S / T |  |
| Alarm Source | 3 terminals input, VMD alarm, Command alarm, Audio detection alarm |  |
| Alarm Actions INPUT/ OUTPUT | SDXC/SDHC/SD memory recording, E-mail notification, HTTP alarm notification Indication on browser, TCP alarm notification output |  |
| Audio Input | ø3.5 mm stereo mini jack For microphone input: Recommended applicable microphone: Plug-in power type (Sensitivity of microphone: -51 dB～-38dB (0 dB=1 V/Pa, 1 kHz)) Input impedance : Approx. 2 kΩ (unbalanced) Supply voltage：2.5 V ±0.5 V For line input：Input level: Approx. –10 dBV |  |
| Audio Output | ø3.5 mm stereo mini jack (Audio output is monaural.) Output impedance: Approx. 600 Ω (unbalanced) Output level: –20 dBV |  |
| External I/O Terminals | ALARM IN 1 (Alarm input 1/ Black & white input/ Auto time adjustment input) (x1) ALARM IN 2 (Alarm input 2/ ALARM OUT) (x1) ALARM IN 3 (Alarm input 3/ AUX OUT) (x1) |  |
| Safety | UL (UL62368-1), c-UL (CSA C22.2 No.62368-1), CE, IEC62368-1 |  |
| EMC | FCC (Part15 ClassA), ICES-003 ClassA, EN55032 ClassA, EN55024 |  |
| Power Source and Power Consumption | PoE++（IEEE802.3bt compliant） |  |
| Ambient Operating Temperature | –40 °C to +55 °C*2 {–40 °F to 131 °F} (Power On range: –20 °C to +55 °C {–4 °F to 131°F}) Maximum temperature according to NEMA TS 2 (2.2.7) : 74℃(165℉) |  |
| Ambient Operating Humidity | 10 to 100 % (no condensation) |  |
| Anti-Condensation System | Temish element |  |
| Water and Dust Resistance | IP67/IP66 (IEC 60529), Type 4X (UL50E), NEMA 4X compliant |  |
| Shock Resistance | IK10 (IEC 62262) |  |
| Other standard support | NEMA TS 2 (2.2.7-2.2.9) |  |
| Dimensions | ø250 mm x 195 mm (H) |  |
| Mass (Approx.) | Approx. 3.8 kg |  |
| Finish | Main body: Aluminum die cast, i-PRO white Outer fixing screws: Stainless steel (Corrosion-resistant treatment) Dome cover: PC resin, Clear |  |