## Slide 1
Outdoor Fixed Network Camera
Panasonic System Networks Co., Ltd.
Security Systems Business Division
WV-SPW532L / WV-SPW312L

## Slide 2: Outdoor Fixed Network Camera
2
  Outdoor-ready with integrated IR
  Clear images in a wide range of lighting conditions
  Full HD/HD at up to 30fps
  IP-Network friendly
  Optional intelligent VMD (i-VMD)
Wide Dynamic Fixed Network camera
WV-SPW312L (720p, 30fps)
WV-SPW532L (1080p, 30fps)

## Slide 3: Outdoor-ready with integrated IR
3
Quick and Easy Installation
The IP66- and NEMA 4X-rated weather-resistant WV-SPW532L/SPW312L outdoor cameras are ready for mounting outdoor and save installation time and costs. The WV-SPW532L/312L can be mounted directly on the wall. Don’t need the base bracket.
Built-in IR illumination
Infrared (IR) illumination is an option for low light or complete darkness conditions. The WV-SPW532L/SPW312L outdoor cameras are equipped with built-in long range IR LEDs which illuminate around 30m (100feet).
Wall mount
Ceiling mount

## Slide 4: Clear images
4
Clear images in a wide range of Lighting conditions
Even a single image can include complex lighting conditions such as bright, glaring, dark and backlight situations. Incorporating advanced image processing technologies, WV-SPW532L/SPW312L camera enables clear and easy identification in a wide range of lighting conditions.
-Multi-process Noise Reduction (MNR)
-Frequency Divided Filter (FDF)
-Super Chroma Compensation (SCC)
-Fog and sandstorm compensation
-High Light Compensation (HLC) and more…
Full HD / HD at up to 30fps
Combining Full HD 1080p / HD 720p resolution and 30fps high frame rate, WV-SPW532L/SPW312L fixed camera enables easy and clear identification of rapid moving objects such as people moving chips and cards in casino, and a vehicle plate on the road.

## Slide 5: Panasonic image processing technologies
5
Fog compensation improves visibility in difficult weather conditions such as fog, sandstorms and more.
Without fog compensation
With fog compensation
Super Chroma Compensation
(SCC) recovers the colors of images, when built-in IR cut filter is removed to enhance light-sensitivity in low light conditions.
With SCC
Without SCC
5-series camera
at 0.04lx
A previous model at 0.04lx
Frequency Divided Filter (FDF) divides the images into multiple frequency ranges, removes the fine noise generated under low illumination for achieving a low bit rate without eliminating edge components.
High sensitivity image sensor with 3D-MNR enables easy identification, capturing color images with low noise in low light conditions.
3D-MNR: 3D Multi process Noise Reduction.
Without FDF
With FDF
High Light Compensation (HLC)
produces clear images, reducing the effect from strong lights such as headlight glare.
Without HLC
With HLC
High-speed Auto Back Focus (ABF) keeps fine focus, controlling precise image sensor position automatically. It streamlines installation and maintenance works.
After ABF
Before ABF

## Slide 6: Panasonic image processing technologies
6
Intelligent Resolution Technology
generates 3M-pixel grade pictures, detecting outlines, detailed texture areas and soft gradation areas and performing optimum processes to each area. (WV-SPW532L)
Lens Distortion Compensation
(LDC) removes the distortion from images caused by wider lens.
Face Wide Dynamic enables clear identification of a person’s face, detecting a facial part in the picture and performing Wide Dynamic automatically.
With LDC
Without LDC
With Face Wide Dynamic
Without Face Wide Dynamic
Variable Image Quality on Specified area (VIQS) saves the network bandwidth and recorder disk space, capturing clear images of region of interest with higher image quality.
Without intelligent resolution technology
With intelligent resolution technology
Higher image quality to region of interest
Lower image quality

## Slide 7: IP-Network friendly
7
Appropriate-sized video stream
Monitors, recorders, smartphones and remote sites such as branches have different requirements for image quality and network bandwidth. WV-SPW532L/SPW312L camera saves the network bandwidth, sending out up to four H.264 (High profile) streams and JPEG streams sized appropriately for each device requirement.
Higher H.264 compression
With the latest UniPhier system LSI, WV-SPW532L/SPW312L camera saves the network bandwidth and the recorder disk space, keeping high quality of images.
Smart coding Technology
Group of Pictures (GOP) control removes unnecessary information from the frame for realizing efficient encoding.
With the latest bitrate reducing technology, GOP control, 3D-MNR and FDF, WV-SPW532L/SPW312L camera saves the network bandwidth and the recorder disk space.
Cameras | WV-SP509 | WV-SPW532L
Full HD at 30fps | 4 Mbps | 3 Mbps ( -25%)
Full HD at 10fps | 4 Mbps | 2 Mbps ( -50%)
Scene | Without GOP | With GOP
Heavy traffic of people | 3 Mbps | 3 Mbps
Minimal traffic of people | 2 Mbps | 1 Mbps(-50%)
When people are walking, I-frame is inserted at regular intervals as usual.
When there is no person walking, I-frames are thinned down to reduce the amount of data.
Predicted
Frame
Predicted
Frame
Predicted
Frame
Generated
code amount

## Slide 8: Optional intelligent VMD (i-VMD)
8
Higher accuracy with more intelligence
Equipped with advanced self-learning algorithm and the latest powerful UniPhier system LSI, WV-SPW532L/SPW312L camera provides high detection accuracy.
Intruder detection
detects people or cars trespassing in restricted areas.
Loitering detection
detects people who has loitered for too long in the area.
Direction detection
detects people or cars that go the wrong direction.
Scene change detection detects tampering with the camera view.
Object detection (removed)
detects objects disappearing that should be present.
Cross line detection
detects people or objects crossing the imaginary lines.
Object detection (left)
detects something left behind that shouldn’t be there.

## Slide 9: … and other useful features
9
Secure SD memory recording
Equipped with a SD memory card slot, WV-SPW532L/SPW312L camera stores recordings locally. Recordings can be password-protected and alteration detection helps ensure credibility of data.
Central management
The WV-ASM200 and System970 i-PRO management software enables central management of the cameras, recorders and monitors.
Viewing on smartphones and tablets
Panasonic Security Viewer enables viewing outside the surveillance center.
View and Setting with various browsers
When the camera is configured and checked, it does not have to be a specific browser such as only IE. Various browsers (Safari, Chrome*, Firefox and IE) can be used.
*The live display is supported only JPEG.
Alarm notification
When VMD, i-VMD, terminal alarm such as door alarm or command alarm is detected, the camera sends alarms to the operators based on pre-configured alert rule and/or saves images to the SD memory card or FTP server.
Privacy masking
The camera supports electronic privacy masking. Zones, the masked areas of the image, are easily defined.

## Slide 10: Specifications
10
 |  | WV-SPW532L | WV-SPW312L
Appearance |  |  | 
Type |  | Outdoor | 
Image sensor |  | 1/3 type MOS Sensor | 
Max. resolution |  | 2,048 x 1,536 | 1,920 x 1,080*1 / 1,280 x 960 *1:Super resolution technology
Max. frame rate |  | 30 fps | 
Day / Night |  | Yes (IR Cut filter Removal) | 
Focus Adjustment |  | ABF | 
Minimum Illumination | Color | 0.07 lx (F1.6) | 0.02 lx (F1.6)
 | B/W | 0.01 lx (F1.6) | 0.006 lx (F1.6)
Wide Dynamic |  | Yes | 
IR LED irradiation distance |  | Approx. 30m (98.43ft.) | 
Vari Focal Length |  | 2.8 mm – 10 mm | 
Angular Field of View (16:9 Mode) | Horizontal | 31° (TELE) – 112° (WIDE) | 28° (TELE) – 102° (WIDE)
 | Vertical | 17° (TELE) – 60° (WIDE) | 16° (TELE) – 55° (WIDE)
Audio |  | N/A | 
SD memory card slot |  | 1 slot (SDXC/SDHC/SD) | 
Ambient Operating Temperature |  | -30°C ~ +50°C (-22 °F ~ 122 °F) | 
Dimension |  | 95 mm (W) x 99 mm (H) x 326 mm (L) {3-3/4 inches (W) x 3-57/64 inches (H) x 1ft 27/32 inches (L)} |