## Slide 1
3-series
Fixed Dome Network Cameras
Panasonic System Networks Co., Ltd.
Security Systems Business Division
WV-SFV311A / WV-SFV310A
WV-SFR311A / WV-SFR310A
WV-SFN311A / WV-SFN310A

## Slide 2: 3+A-series Fixed Dome Cameras
2
  133dB Wide Dynamic Range and 0.01 lux High Sensitivity for color images
  HD 720p at up to 60fps
  IP-Network friendly
  Intelligent VMD (i-VMD)
  Tough design and flexible installation
Super Dynamic Fixed Dome Network camera
WV-SFV311A (D/N (IR))
WV-SFV310A (D/N (Electrical))
Outdoor vandal resistant
WV-SFR311A (D/N (IR))
WV-SFR310A (D/N (Electrical))
Indoor vandal resistant
WV-SFN311A (D/N (IR))
WV-SFN310A (D/N (Electrical))
Indoor

## Slide 3: Clear images
3
133dB Wide Dynamic Range
Even a single scene includes complex lighting conditions such as bright light, the dark of night, high contrast scenes and backlight situations. Incorporating Enhanced Super Dynamic of 133dB wide dynamic range, new 3-series cameras enable clear and easy identification in high contrast scenes and backlight situations.
0.01 lux High Sensitivity for color images
The latest image sensor technology combined with Multi process Noise Reduction (MNR) and Frequency Divided Filter (FDF) results in a high sensitivity of 0.01 lux in clearer color images than ever before. 3-series cameras deliver clear color images even with minimum ambient light like a quarter moon.
HD 720p at up to 60fps
Combining HD 720p high resolution and 60fps high frame rate, 3-series cameras capture rapid moving objects such as people moving chips and cards in casino, bill in the bank and a vehicle plate on the road.
Entrance in a backlight situation
Low lighting scene
Roulette table

## Slide 4: Panasonic image processing technologies
4
Enhanced Super Dynamic
delivers a wide dynamic range of 133dB. With new variable exposure and shutter speed control, Enhanced Super Dynamic captures multiple images with optimal short and long exposures. Enhanced Super Dynamic combines them into one frame and results in clear images.
High Light Compensation (HLC)
produces clear images, reducing the effect from strong lights such as headlight glare.
Frequency Divided Filter (FDF) divides the images into multiple frequency ranges, removes the fine noise generated under low illumination for achieving a low bit rate without eliminating edge components.
Fog compensation
improves video quality in difficult weather conditions such as fog, sandstorms and more.
With Enhanced Super Dynamic
Without HLC
With HLC
Without Enhanced Super Dynamic
Without fog compensation
With fog compensation
Super Chroma compensation
(SCC) recovers the colors of objects, when built-in IR cut filter is removed to enhance light-sensitivity in low light conditions.
With SCC
Without SCC
High sensitivity image sensor with 3DMNR enables easy identification, capturing color images with low noise in low light conditions.
3D-MNR: 3D Multi process Noise Reduction.
3-series camera
Previous model
Without FDF
With FDF

## Slide 5: Panasonic image processing technologies
5
Auto Back Focus (ABF)
keeps fine focus, controlling precise image sensor position automatically. It streamlines installation and maintenance works.
Face Super Dynamic
enables clear identification of a person’s face, detecting a facial part in the picture and performing Super Dynamic automatically.
After ABF
Before ABF
With Face Super Dynamic
Without Face Super Dynamic
Variable Image Quality on Specified area (VIQS) saves the network bandwidth and recorder disk space, capturing clear images of region of interest with higher image quality.
Higher image quality to region of interest
Lower image quality
Wide range built-in IR LED
with active LED control enables easy and clear identification in low light condition, illuminating broad area evenly with infrared (IR) light.
(WV-SFN311L)
Wide illuminated range
Adaptive Black Stretch (ABS)
enables clear identification of people and objects in the dark areas by compensating the signal level automatically.
Lens Distortion Compensation
(LDC) removes barrel distortion from images caused by wide angle lens.
With LDC
Without LDC
With ABS
Without ABS

## Slide 6: IP-Network friendly
6
Appropriate-sized video stream
Monitors, recorders, smartphones and remote sites like branches have different requirements for image quality and network bandwidth. 3-series cameras save the network bandwidth, sending out multiple H.264 and JPEG streams sized appropriately for each device requirement.
Higher H.264 compression
With powerful UniPhier system LSI, 3-series cameras save the network bandwidth and the recorder disk space, keeping high image quality.
Smart coding Technology
Group of Picture (GOP) control removes unnecessary information from the frame for realizing efficient encoding.
With the latest bitrate reducing technology, GOP control, 3D-MNR and FDF, 3 series camera saves the network bandwidth and the recorder disk space.
Cameras | WV-SF/SW3xx | 3-series
HD at 30fps | 4 Mbps | 2 Mbps ( -50%)
HD at 10fps | 3 Mbps | 1 Mbps ( -66%)
(frame rate priority mode)
Scene | Without GOP | With GOP
Heavy traffic of people | 3 Mbps | 3 Mbps
Minimal traffic of people | 2 Mbps | 1 Mbps(-50%)
When people are walking, I-frame is inserted at regular intervals as usual.
When there is no person walking, I-frames are thinned down to reduce the amount of data.
Predicted
Frame
Predicted
Frame
Predicted
Frame
Generated
code amount

## Slide 7: Optional intelligent VMD (i-VMD)
7
Intruder detection
detects people or cars trespassing in restricted areas.
Loitering detection
detects people who has loitered for too long in the area.
Direction detection
detects people or cars that go the wrong direction.
Scene change detection detects tampering with the camera view.
Object detection (removed)
detects objects disappearing that should be present.
Cross line detection
detects people or objects crossing the imaginary lines.
Object detection (left)
detects something left behind that shouldn’t be there.
Intelligent VMD (Optional)
With the latest intelligent Video Motion Detection (i-VMD) technology, 3-series cameras improve the efficiency and effectiveness of surveillance. The evolved self-learning algorithm and powerful UniPhier system LSI results in the high detection rate with less false alerts.

## Slide 8: Tough design and flexible installation
8
IP66-, NEMA-4X and IK10-rated robustness
The WV-SFV3xx outdoor cameras are IP66-, NEMA 4X- and IK10-rated weather and impact resistant. The WV-SFR3xx indoor cameras are IK10-rated impact resistant.
The built-in dehumidification unit keeps 3-series cameras in good running order for many years, preventing water and moisture from penetrating inside the camera.
Flexible installation
The wider tilt angle of lens up to 85° and distortion-free dome design enables lower pace installation than current models. With the WV-Q7118 Sun shade, 3-series outdoor cameras can be mounted on walls easily and quickly.
WV-SFV311 with Sun shade
Improved image quality at upper angle.
85°
Improved image
quality

## Slide 9: Easy installation
9
Easy mounting
The new mounting attachment enables easy installation. Once the attachment plate is secured on the celling, the camera can be fixed tightly just by rotated around 15°. Three installation, 2-gang junction box, with base bracket and direct mounting, are available.
With the non-screw lock Pan-Tilt-Yaw (PTY)
mechanism, it is easy to adjust the viewing
direction.
Base bracket
Attachment plate
Rotate the camera to lock.
(WV-SFV311/310)

## Slide 10: Easy installation
10
Quick setup
Packaging box
When you kit Panasonic network cameras,
WV-SFV311A/310A can be setup without opening the packaging box. You can pick out LAN connector from the packaging box of WV-SFV311A/310A, and can set the basic configuration.
Quick setup tool (PC application)
When you deploy a lot of Panasonic network cameras on the site, Panasonic Security System Configuration Tool (PSSCT) makes it easy to configure and manage them.
Panasonic Security System Configuration Tool (PSSCT)

## Slide 11: … and other useful features
11
SD memory card slot
Equipped with a SD memory card slot, new 3-series cameras store recordings locally on the SD card.
Central management
The WV-ASM200 i-PRO management software or System 970 manage the cameras and recorders at the central surveillance center.
Mobile monitoring Viewing
Panasonic Security Viewer enables viewing live and recorded videos on the smartphone and tablet.
View and Setting on Browser
When the camera is configured and checked, it does not have to be a specific browser such as only IE. Various browsers (Safari, Chrome*, Firefox and IE) can be used.
*The live display is supported only JPEG.
Alarm notification
When VMD, i-VMD, terminal alarm such as door alarm or command alarm is detected, the camera sends alarms to the operators based on pre-configured alert rule and/or saves images to the SD memory card or FTP server.
Privacy masking
The camera supports electronic privacy masking. Zones, the masked areas of the image, are easily defined.

## Slide 12: Optional accessories
12
 | WV-Q169A | WV-Q174B | WV-Q105A
Ceiling Mount Bracket |  |  | 
Compatibility | WV-SFV311A WV-SFV310A | WV-SFR311A WV-SFR310A WV-SFN311L WV-SFN311A WV-SFN310A | WV-SFR311A WV-SFR310A WV-SFN311L WV-SFN311A WV-SFN310A
 | Smoke Dome Cover WV-CW7S | Smoke Dome Cover WV-CR1S | Smoke Dome Cover WV-SF5SA | Sun Shade WV-Q7118
Dome cover |  |  |  | 
Compatibility | WV-SFV311A WV-SFV310A | WV-SFR311A WV-SFR310A | WV-SFN311L WV-SFN311A WV-SFN310A | WV-SFV311A WV-SFV310A
Ceiling Mount Bracket
Dome cover

## Slide 13: Specifications
13
 |  |  |  | WV-SFV311A | WV-SFV310A | WV-SFR311A | WV-SFR310A | WV-SFN311L | WV-SFN311A | WV-SFN310A
Type |  |  |  | Outdoor Vandal resistant |  | Indoor Vandal resistant |  | Indoor |  | 
Image sensor |  |  |  | 1/3 type MOS Sensor |  |  |  |  |  | 
Max. resolution |  |  |  | 1,920 x 1,080*1 / 1,280 x 960 *1:Super resolution technology |  |  |  |  |  | 
Max. frame rate |  |  |  | 60 fps |  |  |  |  |  | 
Day / Night |  |  |  | D/N (ICR) | Electrical | D/N (ICR) | Electrical | D/N (ICR) | D/N (ICR) | Electrical
Minimum Illumination |  | Color |  | 0.01 lx |  |  |  |  |  | 
 |  | B/W |  | 0.003 lx | 0.008 lx | 0.003 lx | 0.008 lx | 0 lx | 0.003 lx | 0.008 lx
Built –in IR LED light |  |  |  | - |  |  |  | Yes | - | 
Angular Field of View | 16:9 mode |  | Horizontal | 28°(Tele) - 99°(Wide) |  | 28°(Tele) - 99°(Wide) |  | 28°(Tele) - 100°(Wide) |  | 
 |  |  | Vertical | 16°(Tele) - 54°(Wide) |  | 16°(Tele) - 54°(Wide) |  | 16°(Tele) - 54°(Wide) |  | 
 | 4:3 mode |  | Horizontal | 28°(Tele) - 99°(Wide) |  | 28°(Tele) - 99°(Wide) |  | 28°(Tele) - 100°(Wide) |  | 
 |  |  | Vertical | 21°(Tele) - 72°(Wide) |  | 21-°(Tele) 72°(Wide) |  | 21°(Tele) - 73°(Wide) |  | 
Audio |  |  |  | Two-way | - | Two-way | - | Two-way |  | One-way Built-in mic.
SD memory card slot |  |  |  | 1 slot (SDXC/SDHC/SD) |  |  |  |  |  | 
Ambient Operating Temperature |  |  |  | -40°C ~ 50°C (-40°F ~ 122°F) |  | -10°C~50°C (-14°F~ 122°F) |  |  |  | 
Dimension |  |  |  | Φ164mm x 139mm (H) {ø6-15/32 x 5-15/32 in. (H)} |  | Φ129.5mm x 102.5mm (H) {ø5-3/32 x 4-1/32 in. (H)} |  | Φ129.5mm x 101mm (H) {ø5-3/32 x 3-31/32 in. (H)} |  |