## Slide 1
WV-SBV131M / SBV111M
Full HD / HD Rugged Mobile Network Camera
Panasonic i-PRO Sensing Solutions Co., Ltd.
Ver. 1.21

## Slide 2: Full HD / HD Rugged Mobile Network Camera
2
  Tough body (Aluminum die cast shell body)
  Wide angle & High Picture Quality
  Easy installation
WV-SBV131M
WV-SBV111M
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent

## Slide 3: Applications
Rugged Mobile Network Cameras are suitable for monitoring on various vehicle:
3
Bus
Train
Large vehicles and cargo vehicle
Armoured car
Wagon
Prisoner monitoring
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent

## Slide 4: Tough body (Compatible with Railway applications )
4
Integrated shell body
MIL-STD-810G
10～2000Hz 7.7G
Wide operating temperature range
The WV-SBV111M/131M operates in temperatures from -40 to +60 degree Celsius.
Outdoor-ready camera
With a polycarbonate camera dome and
aluminum die-cast body, the IP66- and
IP6K9K*-rated weather-resistant.
WV-SBV111M/131M outdoor cameras are ready
for mounting outdoor.
*High temperature and pressure washing water
IK10（20J） TEST *5kg（H=45cm）
The camera conforms to the outdoor harsh environment
Unbreakable, even if shocked externally ;
The WV-SBV111M/131M camera is IK10-rated impact resistant. In case the camera is subjected to mechanical shock, an impact-resistant aluminum die-cast body protects the optical system from the impact.
Then WV-SBV111M/131M can withstand severe shock and vibration since these cameras comply with EN50155 and Mil standard.
Fend off the car wash machine and street trees by vehicle integrated structure.
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent

## Slide 5: Tough body (Scratch Resistant Dome)
5
Test results
■ In preparation for excessive external factors, Dome treated as consumables.
■ No scratches occur to affect the image quality
CAR WASHING BRUSH
Camera
Hard camera dome-cover coating which can bear over 8,540 cycles (7 years) of a harsh washing machine. (Hard coating Level: 2H)
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent

## Slide 6: Wide angle (Back installation)
6
Back installation
Pan0° tilt45° yaw0°
Installation on the bus
2.5m
Road
20m
4:3
16:9
SBV131M [16:9] H: 109°V: 73°, [4:3] H: 97° V:79°
SBV111M [16:9] H: 104°V: 69°, [4:3] H: 104°V: 85°
SBV111M
20m
It covers the 20m (65ft) from the Bus body end to leave a reliable proof images
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent

## Slide 7: Wide angle (Side installation)
7
Side installation
Pan55° tilt40° yaw125°
Pan75° tilt40° yaw20°
Installation on the bus
2.5m
Front door of bus
Front door of bus
11m（ Until the bus back）
Road
11m（ Until the bus back）
Road
4:3
16:9
4:3
16:9
SBV111M
11m(36ft)
Set to the required angle of view without changing the installation position of the camera
It covers backward 11m (36ft) from the front bus door to eliminate the blind spot
SBV131M [16:9] H: 109°V: 73°, [4:3] H: 97° V:79°
SBV111M [16:9] H: 104°V: 69°, [4:3] H: 104°V: 85°
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent

## Slide 8: High Picture Quality at low light condition
8
HLC:OFF ABS:OFF
HLC: ON, ABS: ON
HLC:ON ABS:OFF
Bright parts are saturated.
Not saturated, but whole image is too dark.
While suppressing saturation of point light source, you can see bright and clear images.
Using HLC + ABS function to suppress the saturation of the car headlights, and correct the dark part.
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent

## Slide 9: Easy Installation
9
Attached to the vehicle
Removal of the paint guard
Removal of the Dome
Adjustment of PTY
Attaching of the Dome
Attaching of the Guard
Easy installation of six steps
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent

## Slide 10: Easy Installation (View Angle Adjustment)
10
PTY mechanism allows you easy angle adjustment
- Adjusting the image rotation (YAW).
Adjust by rotating per 5° using the Ⓐ lens adjuster (accessory). *The spots are set up by 10° as the scale mark.
● image rotation (YAW) angle: ±170°
- Adjusting the horizontal (PAN)
You can adjust the rotation per 5° by grasping the left and right side of the lens part with your fingers and rotating it. *The spots are set up by 30° as the scale mark.
● Horizontal (PAN) angle: ±170°
- Adjusting the vertical (TILT)
You can adjust the rotation per 5° by grasping the left and right side of the camera part with your fingers and rotating it. *The spots are set up by 30° as the scale mark.
● Vertical (TILT) angle: ±90°
An angle of view can be adjusted in the direction you want to see, even if installing a camera in various directions.
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent

## Slide 11: Specifications
 | WV-SBV131M | WV-SBV111M
Max. Output Resolution | 1920 x 1080 / 2048x1536 | 1280x720 / 1280 x 960
Lens | 1.95mm (F2.2) | 1.95mm (F2.2)
Angular field of view | [16:9] H:109°, V:73° [4:3] H: 97° , V:79° | [16:9] H:104°, V:69° [4:3] H:104°, V:85°
Adjust angle | PAN:±170°, TILT:±90°, YAW:±170° | PAN:±170°, TILT:±90°, YAW:±170°
Min. Lux (CLR) | 0.1 lx (F2.2) | 0.04 lx (F2.2)
IRLED | No | No
WDR | Yes | Yes
SD Slot | Yes | Yes
Operating temperature | -40℃ to +60℃ *Power On range: –30 °C to +60 °C | -40℃ to +60℃ *Power On range: –30 °C to +60 °
Shock Resistant | IK10 | IK10
Waterproof | IP66, IP6K9K | IP66, IP6K9K
Other standard | EN50155-T3, ECE-R10 (E approval), MIL-STD-810G standard Compliant | EN50155-T3, ECE-R10 (E approval), MIL-STD-810Gstandard Compliant
Power source | PoE (M12) | PoE (M12)
11
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent