## Slide 1: V-SERIES Ultra 4K cameras
WV-V1170
Security Systems Business Division
Panasonic System Networks Co., Ltd.
Notes: 摂氏→華氏 F=(9/5)*C + 32 華氏→摂氏 C=(5/9)*(F-32)

## Slide 2: Indoor Ultra 4K Camera
12MP Ultra 4K Fixed camera
Enables monitoring wide and distant area with 12MP resolution (20fps) / Ultra 4K resolution (25/30fps) by 1/1.7” 12Megapixel CMOS.
Can reduce the network bandwidth and the recorder disk space by H.265 compression. These cameras can also deliver H.264 and MJPEG stream.
Equipped with a microphone.
Equipped with a micro SD memory card slot, WV-V1170 camera stores recordings locally. It is supported up to 128GB.
WV-V1170
(12MP/ 20fps, 4K/ 25/30fps)
Distance 200 m, With CBC lens (25-135mm)
Notes: 288kmph= カトリーナ：280 km/h
伊勢湾台風=270km/h

## Slide 3: Sample System configuration diagram with Panasonic recorder
Site-A
HQ
Management Software
WV-ASM300 series
WJ-ND400/
NV300/NV200
i-PRO camera
V-SERIESE
Rec
+
Playback
Live
*The system supports only H.264 stream of V-SERIES cameras.
*Not every functions of i-PRO camera are supported by V-SEREISE cameras.
*V-SERIES cameras can connect to WV-ASM300 only via recorder.
Live, playback
Live,Rec
Live, Playback
*WV-ASM300 will be released on Feb, 2017.

## Slide 4: Sample System configuration diagram with Video Insight
Site-A
HQ
Video Management Server
i-PRO camera
V-SERIESE
+
Live, Rec
*The system supports only H.264 stream of V-SERIES cameras.
*Not every functions of i-PRO camera are supported by V-SEREISE cameras.
Live, playback
Site-B
i-PRO camera
V-SERIESE
+
Live, Rec

## Slide 5: Specifications
 |  | WV-V1170
Type |  | Indoor
Image sensor |  | 1 / 1.7 type MOS
Max. video resolution (pixel) |  | 4000 x 3000
Max. frame rate |  | 4000 x 3000 : 20fps 3840 x 2160 : 25/30 fps
Day / Night |  | Yes (ICR)
Minimum Illumination | Color | 0.02 lx* (F1.4, Maximum shutter: 10/30s, AGC: 100)：Converted value 0.2 lx (F1.4, Maximum shutter: 1/30s, AGC: 100) * Color： 0.02 lx / F1.4 corresponds to 0.01 lx / F1.2
 | B/W | 0.0002 lx (F1.4, Maximum shutter: 10/30s, AGC: 100)：Converted value 0.002 lx (F1.4, Maximum shutter: 1/30s, AGC: 100)
Lens |  | C / CS
SD memory card slot |  | 1slot (Micro SD)
Ambient Operating Temperature |  | -30°C ~ +50°C
Power Supply |  | DC12V / AC24V, PoE
Dimension |  | 74 (W) x 135 (D) x 66 (H) (mm)
Area selling products as of Dec 2016 (North America, Russia, Latin America, Asia, Middle East) |  | North America, Russia

## Slide 6: Option Lens Information
 | CBC: EG5Z2518FC-MP | Fujinon: DV4x12.5SR4A-SA1L | Ricom: HV03617D_IR-S | Fujinon: DV2.2x4.1SR4A-SA2L
Focal length | f=25-135mm | F=12.5-50mm | f=3.6-17mm | f=4.1-9mm
Iris range | F1.8 | F1.6 | F1.5 | F1.6
Resolution | 3Mp | 5Mp | 4K | 6Mp
Mount | C-Mt* | C-Mt* | CS-Mt | CS-Mt
Angle of view | H:16.2-3.1 V:12.0-2.4 | H:32.54-8.14 V:24.37-6.13 | H:105-27 V:57-15 | H:100.1-45.17 V:74.21-33.59
Focus range | 1.5m-inf. | 0.8m-inf. | 0.3m-inf. | 0.3m-inf.
Type | 1/1.8” | 1/1.8” | 1/1.8” | 1/1.8”
* The C-Mt adapter is included with the camera (V1170).