## Slide 1: V-SERIES IR-PTZ cameras
WV-V6430L
Security Systems Business Division
Panasonic System Networks Co., Ltd.
Notes: 摂氏→華氏 F=(9/5)*C + 32 華氏→摂氏 C=(5/9)*(F-32)

## Slide 2: Outdoor IR-PTZ Camera
2MP Full HD 30x WDR IR PTZ dome camera
Enables zooming in on distant people and objects clearly with 30x optical with extra zoom.
Can reduce the network bandwidth and the recorder disk space by H.265 compression. These cameras can also deliver H.264 and MJPEG stream.
Enables easy and clear identification of moving objects, combining Full HD 1080p resolution and 50/60fps high frame rate.
Be equipped with built-in long range IR LEDs which illuminate around 150m (AC 24V).
Be IP66-rated weather resistant.
Equipped with a micro SD memory card slot, WV-V6430L camera stores recordings locally. It is supported up to 128GB.
WV-V6430L
(1080p, 50/60fps, IR-LED)
IR-LED: ON, 150m
Notes: 288kmph= カトリーナ：280 km/h
伊勢湾台風=270km/h

## Slide 3: Sample System configuration diagram with Panasonic recorder
Site-A
HQ
Management Software
WV-ASM300 series
WJ-ND400/
NV300/NV200
i-PRO camera
V-SERIESE
Rec
+
Playback
Live
*The system supports only H.264 stream of V-SERIES cameras.
*Not every functions of i-PRO camera are supported by V-SEREISE cameras.
*V-SERIES cameras can connect to WV-ASM300 only via recorder.
Live, playback
Live,Rec
Live, Playback
*WV-ASM300 will be released on Feb, 2017.

## Slide 4: Sample System configulation diagram with Video Insight
Site-A
HQ
Video Management Server
i-PRO camera
V-SERIESE
+
Live, Rec
*The system supports only H.264 stream of V-SERIES cameras.
*Not every functions of i-PRO camera are supported by V-SEREISE cameras.
Live, playback
Site-B
i-PRO camera
V-SERIESE
+
Live, Rec

## Slide 5: Specifications
 |  | WV-V6430
Type |  | Outdoor PTZ
Image sensor |  | 1 / 2.8 type MOS
Max. video resolution (pixel) |  | 1920 x 1080
Max. frame rate |  | 50/60 fps
Day / Night |  | Yes (ICR)
Minimum Illumination | Color | 0.004 lx (F1.6, Maximum shutter: 1/1s, Gain: 100)* 0.13 lx (F1.6, Maximum shutter: 1/30s, Gain: 100)
 | B/W | 0 lx (F1.6, Maximum ｓhutter: 1/30 s, Gain: 100, when the IR LED is lit) 0.0002 lx (F1.6, Maximum shutter: 1/1s, Gain: 100)* 0.005 lx (F1.6, Maximum shutter: 1/30s, Gain: 100)
Built –in IR LED irradiation distance |  | AC24V : Approx. 150m
Focal Length |  | 4.5 - 135mm (30x Optical zoom)
SD memory card slot |  | 1slot (Micro SD)
Ambient Operating Temperature |  | -30°C ~ +55°C
Dimension |  | Φ 186 x 310 (mm)
Area selling products as of Dec 2016 (North America, Russia, Latin America, Asia, Middle East) |  | Russia, Latin America, Asia, Middle East
* Converted value