## Slide 1
Coaxial-LAN Converter
WJ-PR201/204
WJ-PC200
Panasonic System Networks Co., Ltd.
Security Systems Business Division

## Slide 2
Coaxial-LAN Converter
2
Receiver side unit
WJ-PR201 (1ch), WJ-PR204 (4ch)
  Reduce the initial cost
  Reduce the installing space
  Can install a camera in the wide area
Camera side unit
WJ-PC200
Coaxial-LAN Converter

## Slide 3
Applications
3
Analog Camera
Network Camera
IP-based system can be realized while reducing the initial setup cost
When using external power for a power supply to camera, can extend 2 kilometers as cabling distance. *when using 1ch center unit
Network camera (using external power)
Up to 2,000 meter*
When many cameras would like to be installed in the around an estate and the outside a building, can use a coaxial-lan.
The space for installing the device is saved
within the switchboard
Space above ceiling plate
of elevator
within
the outdoor housing
Replace an analog camera with a network camera using existing coaxial-Lan cable
Extend cabling distances when installing cameras in a wide area
For exterior installation
Small size for various install location

## Slide 4
Reduce the initial cost
4
Existing coaxial-Lan cable can be used
You can construct IP-based system using the latest products without adding a wiring work of Network cable if you use WJ-PR201/204 and WJ-PC200.
No additional wiring work for cameras
DVR
NW Switch
LAN
LAN
LAN
LAN
LAN
NWDR
WJ-PR204
WJ-PC200
*When using PoE function for supplying power to camera, total energy consumption should be 40W or less. If it is more than 40W, supply power to camera separately.

## Slide 5
Reduce the initial cost
5
WJ-PR201/PR204
PoE NW Switch
LAN (up to 5m)
or
Power over coaxial cable
Almost all Panasonic cameras including Outdoor PTZ cameras can be supplied power from WJ-PR201/PR204 which comply with the PoE+. WJ-PR204 supplies 40W as the maximum supply power of the 4-channel total, and WJ-PR201 supplies up to 30W.
WJ-PR201/PR204
Receiver side unit can work with PoE
WJ-PR201/PR204 can be supply power from PoE Hub. Even if there is a location where the power supply from AC adapter is difficult, you can install the camera using WJ-PR201/204.
No additional power source construction
AC adapter

## Slide 6
Reduce the installing space
6
The coaxial-LAN converter is downsized.
The size of WJ-PC200 is the two third size as the size of the conventional model (BY-HPE11KT). Also as a space was difficult to install up to now, you can install the camera by using WJ-PC200.
The size of WJ-PR201/204 is the one half size as the size of the conventional model (BY-HPE11KT). When using WJ-PR204, you can house 16 cameras (four-channel x four units) in 1U on the rack.
Install it in the narrow space
within the switchboard
Space above ceiling plate
of elevator
within the outdoor housing
: 76x76x35
WxHxD (mm) : 79x115x35
Conventional ratio
2/3
Conventional ratio
1/2
: 105x44x98
WxHxD (mm)
: 105x44x208

## Slide 7
Can install a camera in the wide area
7
When a camera would like to be installed in the outside a building or extend a cable distance, LAN cable cannot be extended over 100 meters. However, using WJ-PR201/PR204 and WJ-PC200 with an AC adapter, you can extend the cable distance to 2 kilometers, and you can monitor the suspicious people/behavior from remote place.
And, this coaxial-LAN converter realizes the high speed communication. TCP:35Mbps or over, UDP: 45Mbps or over. (using 5C-2V, RG-6/U or equivalent. the communication distance is 2 kilometers or less. when using WJ-PR204, this speed is the total value of four-channels)
Cable extension maximum 2 kilometers
LAN：
Up to 100 meters
camera
PoE
LAN
Coaxial-Lan: Up to 2 kilometers
(using 5C-2V cable, RG-6/U or equivalent and WJ-PR201 for receiver side)
PoE
LAN
LAN
NWDR
WJ-PC200
WJ-PR201

## Slide 8
Specifications
8
 |  | WJ-PC200 | WJ-PR201 | WJ-PR204
Type |  | Camera side | Receiver side | 
Communication system |  | Limitation method (HD-PLC) |  | 
Transmission speed |  | 35 Mbps (TCP)/45 Mbps (UDP) or over *Transmission distance is 2 kilometers or less. *The speed of using WJ-PR204 is the total value of 4-ch. |  | 
Connector | BNC | 1 | 1 | 4
 | 100BASE-TX | 1 | 1 | 1
Max. transmission distance (RG-6/U) | PoE power supply | - | 500 m (1,640 feet) with Panasonic camera 300 m (984 feet) without Panasonic camera | 
 | PoE+ power supply | - | 300 m (984 feet) with Panasonic camera 200 m (656 feet) without Panasonic camera | 
 | Without PoE power supply | - | 2,000 m (6,561 feet) | 500 m (1,640 feet)
Ambient Operating Temperature |  | -10°C ~ +50°C (+14°F ~ 122°F) | 0°C ~+50°C (+32°F ~ 122°F) | 
Dimension (W x H x D) |  | 76 mm x 76 mm x 35 mm | 105 mm x 44 mm x 98 mm | 
Power supply |  | - | AC adapter and AC Cord *UK and other types of AC cords are included. |