## Slide 1: 5MP H.265 360-Degree Camera
WV-S4150 (Indoor model)
WV-S4550L (Outdoor Vandal Resistant model)
WV-S4550LM (Outdoor Vandal Resistant Transit model)
Ver. 1.02
Panasonic i-PRO Sensing Solutions Co., Ltd.

## Slide 2: Concept & Main Features
New i-PRO extreme camera enables high performance 360-degree surveillance
2
High resolution at 360-degree surveillance area
Intelligent Auto / High sensitivity with built-in IR LED
Super dynamic 108dB
Extreme Visibility
Extreme Compression
H.265 compression with new Smart coding technology
Extreme Data Security
Secure communication with Symantec certification
Extreme Analytics
Intelligent VMD and video analytics
Extreme Reliability
Vandal resistant / IP66 compliant

## Slide 3: Extreme Visibility
5MP High resolution at 360-degree surveillance area
Enables sharp rendering image of objects and people’s face
New i-PRO extreme
3
Leading brand
6m
Less distortion

## Slide 4: Extreme Visibility
Automatically optimizes camera parameters for best tuned image for various scenes, using techniques like Full Auto Shutter & Iris control, Backlit compensation , auto image stabilization.
Also can detect characteristics and movement within the scene to optimize camera settings to provide best fit picture quality.
Intelligent auto mode sharp images of moving objects
Leading brand
(5MP)
New i-PRO extreme
with iA
(5MP)
4

## Slide 5: Extreme Visibility
High sensitivity with built-in IR LED ex. still picture image
Enables to visible objects with built-in IR light even 0 lux of dark condition
New i-PRO Extreme
6m
10m
Leading brand
6m
10m
5

## Slide 6: Extreme Visibility
High sensitivity with built-in IR LED ex. moving picture image
Enables to visible objects with built-in IR light even 0 lux of dark condition
New i-PRO Extreme
Leading brand
6

## Slide 7: Extreme Visibility
Super dynamic 108dB
Both bright and dark area are visible by super dynamic function.
Leading brand (5MP)
New i-PRO extreme with SD (5MP)
7

## Slide 8: Extreme Compression
30fps
15fps
7.5fps
3ps
1ps
32sec
64sec
160sec
480sec
16sec
4sec
1ps
480sec
4sec
Smart coding Technology
With the latest bitrate reducing technology, GOP control with new frame rate control , Auto-VIQS, these cameras save the network bandwidth and the recorder disk space. The cameras can reduce the amount of data by up to approx. 95% for still scene and up to approx. 80% for moving scene compared with the normal H.264 codec. When comparing with Panasonic H.264 camera (WV-SF438 etc) , the amount of data is reduced by up to approx. 70% for moving scene and up to approx. 90% for still scene.
I-frame is inserted
at regular intervals as usual.
I-frames are thinned down
to reduce the amount of data.
*Simulated image
Automatically determine areas with and without motion
and reduce the data volume of those without motion.
Reduces encoding data by using p-frame in place of i-frame
when no motion is detected.
8
GOP control
Auto-VQOS
Low Bitrate
(Higher
Compression)
Mid. Bitrate
(Original compression)
Generated
code amount
Predicted
Frame
Predicted
Frame
Predicted
Frame
WITH MOTION
WITHOUT MOTION
New
frame rate control
The I-frames refresh interval is depending on the presence or absence of motion, the bit rate at the time of scene shooting without motion is further reduced. (Max. I-frames refresh interval/480sec, 1fps)
With
Motion
Without
motion
With
Motion

## Slide 9: Extreme Compression With 5MP models
9
95%
50%
Server/HDD OPEX , No need for special network
Solution!
Reduce TCO
H.264
New H.265 i-PRO extreme
New H.265 i-PRO extreme
with smart coding

## Slide 10: Extreme Data Security
Protect the devices from cyber attacks
Prevention leakage of the data
on communication network
Eliminated vulnerability with the latest CVE* support
*CVE : Common Vulnerabilities and Exposures. Common Vulnerabilities and Exposures is a dictionary of common names
(i.e., CVE Identifiers) for publicly known
Realize secure communication between devices by using communication encryption (SSL/TLS communication).
Panasonic cameras deliver the encrypted video, and it‘s stored in WJ-NX200K (Panasonic recorder).
The data can be password-protected and alteration detection helps ensure credibility of data.
Prevention leakage of the video
The stream and video are encrypted by the module meet FIPS140-2 level 1 CAVP*. Panasonic fully protect the stream and the video on the End-to-End System.
*Evaluated by WV-TW370P
By using hash value, can detect Video alteration.
*When using this function, you need optional licenses.
Secure Communication
10

## Slide 11: Extreme Analytics
Behavior Analysis / Privacy Protection
11
Analyze high-traffic and long-stay zones
Heat Mapping
Moving Object Removal
Remove people and moving
objects from the video
Take a head count
of visitors
People Counting
*With optional software WV-SAE200
11
Notes: Vandal Resistant
Pan angle up to 100 degree for outdoor box model.
Salt (Corrosion)-resistant screw

## Slide 12: Extreme Analytics - Intelligent VMD
Detect various abnormal behavior of person by Optional intelligent VMD (i-VMD) software WV- SAE200
12

## Slide 13: Extreme Reliability
Highly impact resistant.
Compliant with IEC 60068-2-75 test Eh,
50 J / IEC 62262 IK10.
Vandal Resistant
Prevention from fixation at maintenance.
Salt (Corrosion)-resistant screw
(All the screws of the outer)
13
Achieves high endurance under extreme condition
Anti-humidity
The built-in electrical dehumidification keeps the camera dry inside, using
electrolysis to remove any moisture from the camera. This anti-humidity
technology is safe and green due to low power consumption
and no heaters or mechanical fans being used.
Water & Dust Resistant
IP66
NEMA 4X compliant.
Notes: Vandal Resistant
Pan angle up to 100 degree for outdoor box model.
Salt (Corrosion)-resistant screw

## Slide 14: Specifications
 |  |  | WV-S4150L | WV-S4550L | WV-S4550LM | 
Image sensor |  |  | 1 / 3” type MOS |  |  | 
Max. video resolution (pixel) |  |  | 2192x2192 (Fish eye) |  |  | 
Max. frame rate |  |  | 30 fps |  |  | 
Video Compression |  |  | H.265 / H.264 / MJPEG |  |  | 
Minimum Illumination *Shutter speed 1/30s |  | Color | 0.3lx @F2.4, 0.02 lx @ shutter speed 16/30 |  |  | 
 |  | B/W | 0.2lx @F2.4, 0.013 lx @ shutter speed 16/30 | 0.04lx @F2.4, 0.0025 lx @ shutter speed 16/30, 0 lx @ IR |  | 
IR LED / Maximum irradiation distance |  |  | - | Yes / 10m |  | 
Angular Field of View | Horizontal/Vertical |  | 186°/ 186° |  |  | 
Audio Compression |  |  | G.726, G.711, AAC-LC |  |  | 
SD memory card slot |  |  | 1slot (SDXC/SDHC/SD) |  |  | 
Zoom Ratio |  |  | Digital zoom (x1, x2, x4) |  |  | 
Wide dynamic range |  |  | Super dynamic 108dB |  |  | 
Smart coding |  |  | Yes |  |  | 
M12 connector / Railway application |  |  | - |  |  | Yes / EN50155-TX
External I/O Terminals |  |  | ALARM IN 1 (Auto time adjustment) (x1), ALARM IN 2 (ALARM OUT) (x1), ALARM IN 3 (AUX OUT) (x1) |  |  | 
Audio input / output |  |  | ø3.5 mm stereo mini jack x 1 / ø3.5 mm stereo mini jack x1 |  |  | 
Water and Dust Resistance |  |  | - | IP66, NEMA 4X compliant |  | 
Shock Resistance |  |  | - | 50J IEC60068-2-75, IK10 (IEC 62262) |  | 
Ambient Operating Temperature |  |  | -10°C ~ +50°C (14 °F ~ +122 °F) | -40°C ~ +50°C (-40 °F ~ +122 °F) @ IR LED ON, -40°C ~ +60°C (-40 °F ~ +140 °F) @ IR LED OFF |  | 
Dimension (mm) / Mass(approx.) |  |  | ø150 mm × 50.5 mm (H) / Approx. 390 g | ø164 mm × 96.3 mm (H) *with the base bracket / Approx. 1.3 kg |  | 
14

## Slide 15: Optional Accessories
15
  Mount brackets
WV-Q124
Mount Bracket
WV-Q121B
Ceiling Mount Bracket
WV-Q122A
Wall Mount Bracket
WV-Q185
Wall Mount Bracket
WV-Q186
Mount Bracket
WV-Q105A
Ceiling Mount Bracket
  WV-S4150
  WV-S4550L/S4550LM

## Slide 16: Applications
Those cameras are suitable under the extreme conditions
16
Retails / Shopping mall
Airport
Train / Subway
Bank
Education / Hospitals
Buildings
Logistics and more.