## Slide 1: Network Video Disk Recorder
WJ-NX200K
【NTSC】
Panasonic i-PRO Sensing Solutions Co., Ltd.
Ver. 1.01

## Slide 2: Concept & Main Features
PC-Less Surveillance Solution
Secure & High Compression Recording
Up to 16 cameras (H.264/H.265) support
384 Mbps Maximum Total throughput
Secure Communication between cameras and WJ-NX200K and between WJ-NX200K and applications
Dual Stream Recording for narrow band network playback
Easy installation & operation
Automatic Security System configuration wizard
Image search with thumbnail
High speed copy to the USB storage
Built-in GUI and Dual HDMI Outputs
High Reliability & Redundancy
Eco-writing : Acceleration of data access (reading/writing) by original filesystem
Momentary power failure resistance
Keep working & recording without UPS within 200ms
H.265/H.264 high-throughput and scalable recorder featuring integrated GUI and
robust embedded IP security enabling a secure end-to-end PC-Less surveillance solution

## Slide 3: Secure & High Compression Recording
WJ-NX200K
Network Video Disk Recorder
16 cameras (H.264/H.265)
384 Mbps Total throughput
WJ-NX200K supports up to 16 cameras. As basic recorder, WJ-NX200K support
9 cameras. When adding a additional license WJ-NXE20(W) in WJ-NX200,
WJ-NX200K supports up to 16 cameras.
In addition, WJ-NX200K can record both H.264 and H.265 stream.
It is easy to configure a coexisting system of i-PRO H.264 cameras and i-PRO H.265 cameras since WJ-NX200K can record both H.264 and H.265 stream.
WJ-NX200 is equipped with maximum 384 Mbps as total throughput. Maximum recording throughput is 192 Mbps, and it is possible to record the images of 16 cameras when connecting Full-HD H.265 camera (30ips, 2 Mbps). Maximum output throughput is 192 Mbps, and the video of 16 all cameras (Full-HD, 30ips, 2M bps) can be output to a monitoring software at one time.
Basic : up to 9 cameras
NXE20
Camera
Additional kit
Add one license (up to 16 cameras)

## Slide 4: Secure & High Compression Recording
Protect the devices from cyber attacks
Prevention leakage of the data
on communication network
Eliminated vulnerability with the latest CVE* support
*CVE : Common Vulnerabilities and Exposures. Common Vulnerabilities and Exposures is a dictionary of common names
(i.e., CVE Identifiers) for publicly known
Realize secure communication between devices by using communication encryption (SSL/TLS communication).
Panasonic cameras deliver the encrypted video, and it‘s stored in WJ-NX200K (Panasonic recorder).
The data can be password-protected and alteration detection helps ensure credibility of data.
Prevention leakage of the video
The stream and video are encrypted by the module meet FIPS140-2 level 1 CAVP*. Panasonic fully protect the stream and the video on the End-to-End System.
*Evaluated by WV-TW370P
By using hash value, can detect Video alteration.
*When using this function, you need optional licenses.
Secure Communication

## Slide 5: Secure & High Compression Recording
Dual Stream Recording for narrow band network playback
WJ-NX200K
WV-ASM300 series
i-PRO H.264 cameras
i-PRO Extreme H.265
2nd stream
1st stream
2nd stream
1st stream
Rec
Rec
Playback
Video delay may be happened as playing a several cameras at one
time or playing on a narrow band. Therefore, WJ-NX200K has
the function which can record 2 stream per a camera.
When using this function, an operator can set the stream
depending on their playback environment.
i.e)
1st stream is recorded at Full-HD resolution and 2nd stream is
recorded at VGA resolution.
・When network band of an operating environment is narrow band.
・When playing the video on WV-ASM300, it plays a video of 1st stream.
・When an operator play a several cameras at one time.
It is possible to use 2nd stream when playing the video on
multiscreen on WV-ASM300.

## Slide 6: PC-Less Surveillance Solution
・Automatic Security System configuration wizard
Camera registration GUI
With only 4-steps “Easy start” of WJ-NX200, the setting of the recorder and cameras is completed in a few minutes from main display (without PC).
Time and date setting
Camera registration
Multi-screen layout setting
Recording image quality setting
Easy installation & operation
・Image search with thumbnail
Easy to find out image by thumbnail search
[Note]
Multiple cameras are not supported
It is necessary to select start date and time and display interval

## Slide 7: PC-Less Surveillance Solution
Built-in GUI and Dual HDMI Outputs
Main display (HDMI)
Equipped with two HDMI output, WJ-NX200 provides PC-less operation that enables users operate just about all features from the main display without running a PC. The main and sub displays support multi-screen viewing. The main display supports up to 4K resolution, and the sub display supports up to Full-HD resolution.
Display | Interface | Viewing live images | Playback videos | Operation and Setting
Main display | HDMI | P | P | P
Sub display | HDMI, BNC | P | - | -
High speed copy to the USB storage
Data copy speed will be 3 times higher than current NVR
NV300
(Current)
Approximately 18.0 Hours
NX200
6.0 Hours
Example
・2 cameras x 48 hours data copy
・ USB3.0
・Smart coding :efficiency of data compression

## Slide 8: High Reliability and Redundancy
Eco-writing : Acceleration of data access (reading/writing) by original filesystem
WJ-NX200K can reduce the movement of a head to the utmost limit to access own HDD since it equips with Panasonic proprietary file system. Thus WJ-NX200K achieves the high efficiency of writing control, and can extend the life of HDDs.
Reduce the movement of a head to the utmost limit
Reduce the movement of a head to the utmost limit
NX200
Reduce fever of actuator motor
Reduce abrasion of motor

## Slide 9: High Reliability and Redundancy
95%* of momentary power failure is a power failure within 200ms. WJ-NX200K doesn’t have UPS, but it doesn’t stop and doesn’t reboot even when occur a instantaneous voltage drop within 200ms.
When a power failure time is longer than 200ms, WJ-NX200K detects a power interruption and shuts safe down by itself.
WJ-NX200K provide a stable recording and a stable operation for you.
*The case of power source conditions in Japan
“Keep working & recording” without UPS
Momentary power failure resistance

## Slide 10: System Configuration
Monitor output
(up to 16 cameras)
ASM300
NW camera
Mobile
Analog camera
NW
Encoder
Decoder
NX200K
Coax-Lan convertor
Monitor
Key-board
Mouse
Basic up to 9 cameras
NXE20
Camera
additional
kit
NXSxx
Secure
Comm.
kit
Software license

## Slide 11: WJ-NX200 Specifications
Supported Cameras | Supported Cameras | Panasonic i-PRO series Network camera
 | Supported Image Format | H.265,H.264,JPEG,
 | Supported Audio Format | G.726 32kbps, AAC-LC 128kbps, G.711 64kbps for Onvif
 | Maximum Number of Cameras | MAX.16
Recording | Recording Mode | Event, Schedule, Emergency
 | Frame Rate/Camera | Up to 60 ips
 | Others | Pre-Event Recording, 2 stream recording
Playback | Main Unit Function | PLAY, Rev PLAY, Pause, Stop, FF, FR, Prev Record, Next Record, Prev Image, Next Image, Go to Date, Go to Last (30 s), Time-saving playback
 | Viewer Software | PLAY, Rev PLAY, Pause, FF, FR, Prev Record, Next Record, Prev Image, Next Image
Data Format/Copy |  | N3R/MP4 *Copy to USB
HDD | Type | 3.5 inch Serial ATA HDD, Up to 2x HDDs can be installed
 | Maximum Capacity | 2 HDD slots Up to 12TB(2x 6TB) will be supported
 | RAID(Software RAID) | RAID 1 supported
Network | Interface | 2x 10BASE-T / 100BASE-TX / 1000BASE-T (RJ45)
 | Maximum Band Width | Total throughput : Max. 384Mbps Recording throughput : Max. 192Mbps, Output throughput : Max. 192Mbps

## Slide 12: WJ-NX200 Specifications
Viewer Software (Additional Functions) | NX Viewer | Alteration detection, Save as JPEG, Two times zoom, Print, Copy, Aspect ratio switching, fish eye correction,
External Interface | Spot Output Connector | 1x 1 V [p-p] / 75 (BNC)
 | Monitor (HDMI) Connector | [Main monitor] HDMI 4K UHD(3840x2160p) /30Hz, 4K UHD(3840x2160p) /25Hz, 1920x1080p /60Hz, 1920x1080p /50Hz, 1920x1080i /60Hz, 1920x1080i /50Hz [Sub monitor] HDMI 1920x1080p /60Hz, 1920x1080p /50Hz, 1920x1080i /60Hz,1920x1080i /50Hz
 | Alarm Connector | Alarm input: 9 / output:1(1x -10 dBV, 600 ohm ,Unbalanced (RCA)
 | USB connector | Front x2: USB3.0 x1 (copy), USB2.0 x1(mouse, keyboard), Rear x2: USB3.0 x1 (copy), USB2.0 x1(mouse, keyboard)
General Specifications | Power Source/Power Consumption | WJ-NX200K/P : 120 V AC, 50 Hz/60 Hz , Approx.56 W
 | Ambient Operating Temperature | +5 °C to +45 °C (41 °F to 113 °F)
 | Ambient Operating Humidity | 5 % to 90 % (no condensation)
 | Dimensions (W x H x D) | 430 mm x 88 mm x 300 mm (16-9/16" x 3-7/16" x 11-13/16“, excluding rubber feet and projections)
 | Weight | Approx.5.2kg (11.5lbs) [without HDD] / Approx.6.6kg (14.5 lbs.) [with 2x HDDs]

## Slide 13: WJ-NX200K optional line-up
Software
Additional Camera kit | WJ-NXE20(W) | Additional channel license(Up to 16 cameras)
Secure Communication license | WJ-NXS16(W) | Secure optional license for 16ch
 | WJ-NXS04(W) | Secure optional license for 4ch
 | WJ-NXS01(W) | Secure optional license for 1ch

## Slide 14: Applications
This recorder is suitable under the extreme conditions :
Banks
Retails / Quick-Service Restaurants
Hospitals
Education
Factories
Gas Stations and more.