## Slide 1
HD PTZ Network Cameras
WV-SC387
WV-SW397/SW397A
Panasonic System Networks Co., Ltd.
Security Systems Business Division

## Slide 2
HD PTZ Network Cameras
2
Indoor
WV-SC387
  Powerful Pan-Tilt-Zoom
  Wide tile angle
  Tough outdoor-ready (WV-SW397)
Weather-resistant outdoor
WV-SW397/SW397A
The Panasonic WV-SW397/SW397A and WV-SC387 PTZ network cameras are high performance PTZ cameras that deliver clear HD 720p images with 105dB wide dynamic range and produce color images with a minimum illumination of 0.3 lux.
The powerful PTZ cameras are suitable for surveillance where broad area coverage and zooming in are required.

## Slide 3
Powerful Pan-Tilt-Zoom
3
Powerful 45x Extra zoom
With the powerful 45x optical with extra zoom, the WV-SC387 and WV-SW397/SW397A PTZ cameras enables zooming in on distant people and objects clearly.
Smooth PTZ operation
With the WV-ASM200 or System970 management system, the WV-CU950 system controller with 3D joystick helps the operator track people and objects, providing smooth and high precision pan/tilt/zoom control.
Auto modes
Auto modes help the operator surveille a broad area, controlling the PTZ camera in a pre-defined sequence;
Auto panning continues to pan in a pre-defined rotation range.
Preset sequence/Patrol automatically changes the PTZ camera direction to pre-defined positions in sequence.
Advanced auto tracking starts panning, tilting and zooming, and keeps the moving object displayed in the center of the monitor when a moving object is found in the camera view.
45x(Optical 30x. EX-Optical 1.5x)
36x(Optical 30x, Ex-Optical 1.2x)
Distance from camera : Approx. 10m

## Slide 4
Wide Tilt angle
4
-25°~205°-tilt indoor camera
The dome cover-less WV-SC387 indoor camera provides extremely wide vertical coverage from -44° to 224°, supporting tilt angle from -25° to 205° and wide angular field of view.
-15°~195°-tilt outdoor camera
The WV-SW397/SW397A outdoor PTZ camera delivers a clear image even when it tilts above the horizontal position. Auto Eyelid Mechanism (AEM) removes extra light that makes the image blurred due to the small curvature difference between the lower spherical part and upper cylindrical part of the camera dome.
Doom cover
upper cylindrical part
lower spherical part
AEM light shield
Auto Eyelid Mechanism (AEM)
-25°
-44°
Wide vertical coverage
AEM is on.
AEM is off.

## Slide 5
Tough, outdoor-ready camera
5
Tough, outdoor-ready camera
With an impact-resistant polycarbonate camera dome and aluminum die-cast body, the IP66- and IK10-rated weather-resistant WV-SW397/SW397A outdoor camera is ready for mounting outdoor and save installation time and costs.
Wide operating temperature range
Equipped with a cooling fan and heater, the WV-SW397/SW397A works in temperatures from -50 to +55 degree Celsius .
Rain-wash coating
The hydrophilic coating on the camera dome keeps visibility in rainy weather, sheeting water off instead of forming droplets that scatter light.
(WV-SW397A)
Rain-wash coating. For comparison, the right half is not coated.

## Slide 6
Specifications
6
 |  | WV-SW397/SW397A | WV-SC387
Type |  | Weather-resistant Outdoor | Indoor
Image sensor |  | 1/3 type MOS Sensor | 
Max. video resolution (pixel) |  | HD (1,280 x 720) / SXVGA (1,280 x 960) | 
Max. frame rate |  | 30 fps | 
Day / Night |  | Yes (IR Cut filter Removal) | 
Minimum Illumination | Color | 0.3 lux | 
 | B/W | 0.04 lux | 
Angular Field of View |  | H: 2.6° – 64.6° (16:9), H: 1.4° – 44.4°(4:3) | H: 2.34° – 65.1° (16:9), H: 1.6° – 45.2°(4:3)
PTZ | Zoom | 30x (Optical), 45x (with Extra zoom) | 
 | Pan/tilt | 360° endless (panning), –15° ~ 195° (Tilting) | 360° endless (panning), –25° ~ 205° (Tilting)
Audio |  | Two-way | 
SD memory card slot |  | 1 slot (SDXC/SDHC/SD) | 
Ambient Operating Temperature |  | -30°C ~ +55°C (-22°F ~ 131°F) with PoE+ | –10°C ~+55°C (14°F ~ 131°F)
Dimension (excluding base bracket) |  | ∅229 mm x 392 mm(H) | ø185 mm × 221 mm (H)