## Slide 1: 5MP H.265 Fixed Network Camera
Panasonic i-PRO Sensing Solutions Co., Ltd.
WV-S2550L (Outdoor Vandal Resistant Dome model)
WV-S2250L (Indoor Vandal Resistant Dome model)
WV-S1550L (Outdoor Vandal Resistant Box model)
Ver. 1.02

## Slide 2: Concept & Main Features
New i-PRO extreme camera with high quality image capturing allows 5MP images to be obtained for evidence even under extreme conditions.
2
5MP high quality resolution
High sensitivity with color night vision
Intelligent Auto / Super dynamic 120dB
ClearSight coating (Option)
Extreme Visibility
Extreme Compression
H.265 compression with new smart coding technology
Extreme Data Security
Secure communication with Symantec certification
Extreme Reliability
Vandal resistant / IP66 compliant / Anti-correction
WV-S2550L
WV-S2250L
WV-S1550L

## Slide 3: Extreme Visibility
5MP High resolution
The i-PRO Extreme 5MP camera can be monitored by 1.3 times in distance and width and 1.8 times in area than FHD.
3
FHD
180 ft
97 ft
5MP
240 ft
130 ft
4K
360 ft
193 ft
Angle of view
30-degree

## Slide 4: Extreme Visibility
5MP High resolution
The i-PRO Extreme 5MP camera can be monitored by 1.3 times in distance and width and 1.8 times in area than FHD.
4
Can visible the people and vehicles
Object size
20 ppf
180 ft
FHD model
WV-S2531
240 ft
5MP model
WV-S2550L
360 ft
4K model
WV-SFV781

## Slide 5: Extreme Visibility
5MP High resolution
The i-PRO Extreme 5MP camera can be monitored by 1.3 times in distance and width and 1.8 times in area than FHD.
5
Can visible the faces and license plates
Object size
40 ppf
90 ft
FHD model
WV-S2531
120 ft
5MP model
WV-S2550L
180 ft
4K model
WV-SFV781

## Slide 6: Extreme Visibility
High sensitivity with color night vision
It shows clear color images in low light condition at night time
6
Under 2-5 lux lighting environment
Leading brand camera
i-PRO Extreme camera WV-S2550L

## Slide 7: Extreme Visibility
Intelligent Auto
iA-Intelligent Auto monitors scene dynamics and motion to adjust key camera settings automatically in real-time reducing distortion such as motion blur
on moving objects.
7
i-PRO Extreme camera WV-S2550L
iA ON
i-PRO Extreme camera WV-S2550L
iA OFF

## Slide 8: Extreme Visibility
Intelligent Auto
iA-Intelligent Auto monitors scene dynamics and motion to adjust key camera settings automatically in real-time reducing distortion such as motion blur
on moving objects.
8
i-PRO Extreme camera WV-S2550L
iA ON
Leading brand camera

## Slide 9: Extreme Visibility
ClearSight coating (Option)
The specially coated (ClearSight) cover surface resists water stains and dust accumulation, reducing the need for periodic maintenance
9
WV-S1550L
WV-CW7SN
WV-S2550L
WV-CW7CN
Optional cover
WV-CW8CN
Optional cover

## Slide 10: Extreme Compression
H.265 compression with new smart coding technology
*Simulated
image
Automatically determine areas with and without motion and reduce the data volume of those without motion.
Auto-VIQS
Low Bit rate
(Higher
Compression)
Mid. Bitrate (Original compression)
Reduces encoding data
by using p-frame in
place of i-frame when
no motion is detected.
GOP control
WITH MOTION
WITHOUT MOTION
30
fps
15
fps
7.5
fps
3ps
1ps
32
sec
64
sec
160
sec
480
sec
16
sec
4
sec
1ps
480
sec
4
sec
New
frame rate control
With
Motion
Without
motion
With
Motion
I-frames are thinned down
to reduce the amount of data.
10
Max.95%
H.264
i-PRO extreme
H.265 + Smart coding
Bit rate reduction

## Slide 11: Extreme Compression
11
H.265 compression with new smart coding technology
Extreme compression allows higher image quality monitoring in the same
network environment.
Leading brand camera
i-PRO Extreme camera WV-S2550L
with smart coding
Max.
95%
H.264

## Slide 12: Extreme Compression
12
H.265 compression with new smart coding technology
Leading brand camera
with bit rate control
i-PRO Extreme camera WV-S2550L
with smart coding
H.264
Max.50%

## Slide 13: Extreme Data Security
Secure communication with Symantec certification
13
End-to-End Data Encryption
- Support full encryption communication
- Camera encryption recording on-the-edge
Symantec Device Certification
- Pre-installed Symantec Certification
- Video tampering detection
FIPS140-2 Level 1 CAVC compliant
(Federal Information Processing Standardization)
- For federal/public safety usage
Vulnerability Assessment
- 3rd party assessment and penetration tests
made to achieve higher security standards

## Slide 14: Extreme Reliability
14
Dustproof Test
Earthquake Test
Lifetime Test
High-Temperature Test
Drop Test
Pressure Test
Waterproof Test
Thunder Test
Box Shaking Test
Static Electricity Test
Achieve high endurance and long life usage under extreme conditions

## Slide 15: Extreme Reliability
Highly impact resistant.
Compliant with 50J IEC60068-2-75
test Eh, (WV-S2550L)
IEC 62262 IK10
Vandal Resistant
Adoption of Anti-corrosion screws prevents to corrosion and improves maintainability.
Anti-corrosion screw
15
Achieves high endurance under extreme condition
Corrosion of screws
Adopt
anti-corrosion
of screws
Water & Dust Resistant *Except WV-S2250L
IP66
IEC60529 measuring standard compatible
Type 4X(UL50)
NEMA 4X compliant
Notes: Vandal Resistant
Pan angle up to 100 degree for outdoor box model.
Salt (Corrosion)-resistant screw

## Slide 16: Extreme Reliability
16
Dehumidifier
Condensation prevention control of “heater” + “FAN”
Waterproof
breathable
material
Anti-humidity with the new dehumidifier method
By controlling the heater, IR-LED heat and FAN blowing against temperature drop inside the camera, the temperature inside the camera is kept properly to prevent dew condensation.
Ｃｕｒｒｅｎｔ
Ｎｅｗ
Notes: Vandal Resistant
Pan angle up to 100 degree for outdoor box model.
Salt (Corrosion)-resistant screw

## Slide 17: Optional Intelligent VMD
Intruder detection
detects people or cars trespassing in restricted areas.
Loitering detection
detects people who has loitered for too long in the area.
Direction detection
detects people or cars that go the wrong direction.
Scene change detection detects tampering with the camera view.
Object detection (removed)
detects objects disappearing that should be present.
Cross line detection
detects people or objects crossing the imaginary lines.
Object detection (left)
detects something left behind that shouldn’t be there.
Detect various abnormal behavior of person by Optional intelligent VMD (i-VMD) software WV- SAE200
17

## Slide 18: Specifications
18
 |  | WV-S2250L | WV-SS2550L | WV-S1550L
Image sensor |  | 1 / 2.8 type CMOS |  | 
Max. video resolution (pixel) |  | 16:9 mode : 3072 x 1728 (Super resolution), 4:3 mode : 3072 x 2304 (Super resolution) |  | 
Max. frame rate |  | 30 fps * 15fps (Super Dynamic: On, Level: 30 or more) |  | 
Minimum Illumination *Shutter speed 1/30s | Color | 0.07lx @F1.3, 0.0044 lx @ shutter speed 16/30 |  | 
 | B/W | 0.04lx @F1.3, 0.003 lx @ shutter speed 16/30, 0 lx @ IR |  | 
Angular Field of View *16:9 mode | Horizontal | 16:9 mode : 33°(Tele) - 103°(Wide), 4:3 mode : 19°(Tele) - 55°(Wide) |  | 16:9 mode : 34°(Tele) - 106°(Wide) 4:3 mode : 19°(Tele) - 57°(Wide)
 | Vertical | 16:9 mode : 33°(Tele) - 103°(Wide), 4:3 mode : 25°(Tele) - 75°(Wide) |  | 16:9 mode : 34°(Tele) - 106°(Wide) 4:3 mode : 25°(Tele) - 77°(Wide)
Intelligent Auto / WDR / Smart coding |  | Yes / Super Dynamic (120dB) / Yes |  | 
Audio Interface / Compression |  | input (ø3.5 mm stereo mini jack x 1, Line x1), Output(ø3.5 mm stereo mini jack x 1) / G.726, G.711, AAC-LC |  | 
SD memory card slot |  | 1slot (SDXC/SDHC/SD) |  | 
Secure communication |  | FIPS 140-2 Level 1 compliant |  | 
External I/O Terminals |  | ALARM IN 1(Alarm input 1/ Black & white input/ Auto time adjustment input) (x1) ALARM IN 2 (Alarm input 2/ ALARM OUT) (x1) , ALARM IN 3 (Alarm input 3/ AUX OUT) (x1) |  | 
Environmental |  | IK10 | IP66, Type 4X(UL50), NEMA 4X compliant Compliant with 50J IEC60068-2-75, IK10 | IP66, Type 4X(UL50), NEMA 4X compliant IK10
Power Source / Ambient Operating Temperature |  | DC12V,PoE -10°C ~ +50°C (14 °F ~ +122 °F) | DC12V, PoE, -40 °C to +60 °C (-40 °F to 140 °F) / IR LED is off (Power On range : –30 °C to +60 °C {–22 °F to +140 °F}) | 
Dimension (mm) |  | ø129.5 mm x 102.5 mm (H) | ø164 mm x 139 mm (H) *When using base bracket | 133 mm (W) x 133 mm (H) x 377 mm (L)

## Slide 19: Optional Accessories
  ■ Optional dome covers and brackets for WV-S2550L
With ClearSight coating
WV-CW7S
Smoke type
Dome Cover
WV-CW7SN
Smoke type
WV-CW7CN
Clear type
19
Sun Shade
WV-Q7118
Wall mount
WV-Q122A
(Light Silver)
WV-Q185
(Light gray)
WV-Q188
(Light Silver)
WV-Q182
(Light gray)
Pole mount
WV-Q189
(Light Silver)
WV-Q183
(Light gray)
Corner mount
WV-Q186
(Light gray)
WV-Q124
(Fine silver)
Ceiling mount
WV-Q121B
(Light silver)
WV-Q169A
Embedded
ceiling mount
WV-Q105A
For indoor
Ceiling mount

## Slide 20: Optional Accessories
20
  ■ Optional indoor dome covers and brackets for WV-S2250L/S1550L
WV-S1550L
WV-S2250L
WV-CR1S
Smoke type
Dome Cover
WV-Q174B
Embedded
ceiling mount
WV-Q105A
Ceiling mount
WV-CW8CN
Clear type
with ClearSight coating
Front panel
WV-Q188
(Light Silver)
WV-Q182
(Light gray)
Pole mount
WV-Q189
(Light Silver)
WV-Q183
(Light gray)
Corner mount

## Slide 21: Industry examples
Those cameras are suitable under the extreme conditions
21
Retails / Shopping mall
Public safety (City / Highway toll / Parking gate)
Transportation (Airport / Train / Subway)
Retail / Bank / Logistics / Education
Hospital / Building
and more.