## Slide 1: Fiber Optic Media Converter Unit
WV-X65F1 (For IR PTZ and outdoor PTZ cameras)
WV-S25F1 (For outdoor Dome and 360-degree cameras)
Ver. 1.01
Panasonic i-PRO Sensing Solutions Co., Ltd.

## Slide 2
Benefit
Why is fiber optic cable used?
2
Oil pipe line
Tunnel
Bridge
Monitoring center
LAN twisted pair cable
Long-distance surveillance applications
To use fiber optic cable
Long distance data transmission with lower data loss
High-speed data communication with wider bandwidth
Higher reliability and lower total cost

## Slide 3: Concept & key point
3
The optional Fiber Optic Media Convertor Unit enables to reduce the installation time and construction of a long distance monitoring system without spending time on selecting and evaluating the optical media converter.
Sold separately
＋
Current
Installation takes time
Selecting and evaluating the optical media converter
New solution
Incorporate an SFP module into mounting bracket
SPF module
Optical media converter
Junction box
Sold separately
Fiber Optic Media Converter Unit
Built-in
optical media converter
Easy installation for waterproofing
To protects against static electricity and dust and maintains high reliability

## Slide 4: Specifications
4
 | WV-X65F1//S25F1
Waterproof | IP66 (IEC 60529)
Shock resistance | IK10 (IEC 62262)
Power source | 24 V AC (50 Hz/60 Hz)
Input power consumption | 24 V AC: 4.8 A / 77 W
Output power consumption | 24 V AC: 4.5 A / 72 W 12 V DC: 1.1 A / 13 W
Operating Temperature | –40 °C to +60 °C {–40 °F to +140 °F} (Power On range: –30 °C to +60 °C {–22 °F to +140 °F})
Humidity | 10 % to 100 % (no condensation)
Dimensions | ø174 mm × 186 mm (H) {ø6-27/32 inches × 7-5/16 inches (H)}
Weight | Approx. 1.6 kg {3.53 lbs} (Including attachment ring (Approx. 200 g {0.44 lbs})
Support specifications for SFP module
SFP Port Type | LC type
Ethernet Speed | 100/1000 Mbps
Supply voltage, current | 3.3 V typical, Max. 300 mA
SFP Cage | Standard mini-SFP cage (For 6.5 mm pitch SFP)
Required SFP’s Bit Error Rate | Max. 10-12
Compatible SFP module
1000Mbps support Model No. (Brand) | Cable type | TX wavelength | Reach | Operating Temperature
GLC-SX-MM-RGD(CISCO) | MMF | 850nm | 500m | 40-85℃ (Industrial type)
GLC-LX-MM-RGD(CISCO) | SMF / MMF | 1310nm | 10km(SMF) | 
J4859D(HP) |  |  |  | -40-85℃
100Mbps support Model No. (Brand) | Cable type | TX wavelength | Reach | Operating Temperature
GLC-FE-100FX-GD(CISCO) | MMF | 1310nm | 2km | 40-85℃ (Industrial type)
GLC-FE-100LX-GD(CISCO) | SMF |  | 10km | 
*For latest information about compatible SFP modules, refer to the https://security.panasonic.com/support/info/ <Control No.: C0504>.

## Slide 5: Support models and optional brackets (1)
5
WV-X65F1
(Fine silver)
Fiber Optic Media Convertor Unit
WV-Q185
(Light gray)
Wall mount
WV-Q122A
(Light Silver)
WV-Q182
(Light gray)
WV-Q188
(Light Silver)
Pole mount
WV-Q183
(Light gray)
WV-Q189
(Light Silver)
Corner mount
Ceiling mount
WV-Q121B
(Light silver)
IR PTZ camera
WV-X6533LN
WV-S6522LN
Outdoor PTZ camera
WV-X6531N/X6511N
WV-S6530N

## Slide 6: Support models and optional brackets(2)
6
WV-Q122A
(Light silver)
Wall mount
WV-Q185
(Light gray)
WV-Q188
(Light silver)
WV-Q182
(Light gray)
Pole mount
WV-Q189
(Light silver)
WV-Q183
(Light gray)
Corner mount
Ceiling mount
WV-Q121B
(Light silver)
H.264 Outdoor camera
WV-SFV781L
H.265 Outdoor
360-degree camera
WV-X4571L(9M)
WV-S4550L(5M)
H.265 Outdoor
Dome camera
WV-S2570L(4K)
WV-S2550L(5M)
WV-S2531LTN/S2531LN(FHD)
WV-S2511LN(HD)
WV-S25F1
(Light gray)
Fiber Optic Media Convertor Unit

## Slide 7: Industry examples
Fiber Optic Media Convertor Unit are suitable in use several long distance surveillance applications
7
City surveillance
Railway
Airport
Boarder
Oil plant
Shipyard
and more……